## Slide 1
PRowhammer:
Propagating Bit-flips from CPU to GPU
CASPER
Pioneering with grit, bit by bit
Artifact Available
Artifact Functional
Result Reproduced
Mrityunjay Shukla Shubham Roy Sayandeep Saha Biswabandan Panda
Indian Institute of Technology Bombay, India
भारतीय प्रौद्योगिकी संस्थान मुंबई
Indian Institute of Technology Bombay
ISCA 2026
Notes: Thank you for the introduction.
I will be presenting our work, PRowhammer: Propagating Bit Flips from CPU to GPU.
This work was carried out as part of the CASPER research group at IIT Bombay, in collaboration with Mrityunjay Shukla and our advisors, Sayandeep and Biswabandan.

## Slide 2
GPUs are ubiquitous
AI/ML Inference
HPC & Scientific
Computing
Cloud Computing
Notes: As you know GPUs have become the backbone of modern computing.
They run large language models, accelerate scientific computing, and power today's AI ecosystem.
To understand the attacks we present, we first need to look at one key architectural feature of GPUs.

## Slide 3
GPU fundamentally relies on CPU memory
What if CPU memory has a vulnerability that an attacker can exploit?
Applications
CUDA Libraries
CUDA Runtime
GPU Driver
cuBLASLt
GGML
DATA
CODE
GPU kernel code stored here
Model weights staged here
Shared libraries mapped via mmap()
Notes: <powerful, autonomous> Despite having their own dedicated DRAM discrete GPUs cannot operate independently.
They are managed entirely by the CPU software stack.
The CUDA runtime maps GPU shared libraries into CPU memory using mmap.
Model weights are loaded into DRAM first.
GPU kernel code — the compiled SASS instructions that actually run on the GPU — lives in CPU’s DRAM until the moment it is transferred to the device.
The GPU is powerful, but it is not autonomous. It fundamentally relies on CPU memory. Everything flows through CPU memory first.

## Slide 4: Rowhammer
Row 4
Row 3
Row 2
Row 1
Aggressor Row
Aggressor Row
Victim Row
Notes: The answer is Rowhammer. A very brief refresher, By repeatedly activating a memory row thousands of times within a refresh interval, an attacker induces bit-flips in the neighboring DRAM cells
Rowhammer exploits a physical property of DRAM. By repeatedly activating a memory row thousands of times within a refresh interval, an attacker induces electrical interference in adjacent DRAM cells.
This interference causes charge leakage, and if enough charge is lost before the next refresh, bits in a neighboring row can flip.
The repeatedly accessed rows are called aggressor rows, and the affected neighboring row is called the victim row.

## Slide 5: Rowhammer
Memory Profiling
Profile DRAM to find location vulnerable to Rowhammer
Memory Massaging
Hammering
Massage victim’s memory allocation to land at a vulnerable location
Hammer the aggressor rows
Any DDR module susceptible to Rowhammer is inherently susceptible to PRowhammer
Notes: <three step  user-level access  vendor deploy mitigation> The attack has three steps:
Profile the DRAM to find physically flipable locations,
Steers the victim's memory allocation so that sensitive data or code lands at those locations
Then hammer the aggressor rows.
The attacker needs only user-level access.
Vendor deploy mitigation but that keeps on getting bypassed, making Rowhammer an open problem.
Any DDR module susceptible to Rowhammer is inherently susceptible to PRowhammer.

## Slide 6
Victim
(GPU Process)
Threat Model
Attacker
(CPU Process)
Vulnerable CPU DRAM
Server
CPU
GPU
1
2
3
Note: Attacker has black-box access to the target ML models (i.e. no knowledge of model architecture or weights)
Notes: <multi-tenant cloud server  black-box access  submit input  no knowledge of model weights  Question : can a CPU-only attack  use Rowhammer >
Our setting is a multi-tenant cloud server, where the attacker and victim share the same physical machine—and therefore the same host DRAM.
The attacker is an unprivileged CPU process with the ability to perform Rowhammer.
The victim is running an ML workload on the GPU, such as image classification or LLM inference.
Importantly, the attacker has only black-box access to the model. They can submit inputs and observe outputs, but they have no knowledge of the model's weights, architecture, or internal state.
So the question is: can a CPU-only attacker use Rowhammer to manipulate a GPU-resident model?

## Slide 7
7
Targets CPU’s DRAM, affects CPU process
Targets CPU’s DRAM, affects GPU process
Targets GPU's DRAM affects GPU process
CPU Rowhammer
PRowhammer
GPU
Rowhammer
Flipping bits [ISCA ’14]
Zenhammer [USENIX Security ’24]
Rambleed [S&P ’20]
TRRespass [S&P ’20]
Flip Feng Shui [USENIX Security ’16]
GPUHammer [USENIX Security ’25]
GDDRHammer [S&P ’26]
Notes: Before I move ahead with the talk let me differentiate our work from the prior work. Prior CPU Rowhammer

## Slide 8
ML Frameworks
PRowhammer: Attack Overview
Large Language Models
CUDA accelerated libraries
cuBLASLt
GGML
…
CODE
DATA
CUDA Library Invoked
Corrupted code transfer
GPU executes and returns
Generates incoherent text
Notes: Let's take the example of an LLM.
Modern LLMs are built on machine learning frameworks that rely on CUDA-accelerated libraries such as cuBLAS and GGML.
When these libraries are loaded, their code in host DRAM.
An attacker can use Rowhammer to corrupt the GPU kernel code stored in those shared library.
Later, when the framework launches a GPU kernel, the corrupted code is transferred from host memory to the GPU.
The GPU then executes this corrupted code, producing incorrect computation results.
These corrupted results propagate through the model and ultimately affect the LLM's output.
As a consequence, the user may observe degraded model behavior, incorrect predictions, or even completely incoherent generated text.

## Slide 9
ML Frameworks
CUDA accelerated libraries
Large Language Models
CUDA accelerated libraries
cuBLASLt
GGML
…
CODE
DATA
Notes: Let me break down the steps further

## Slide 10
CUDA accelerated libraries
cuBLASLt
Shared library
cublasSaxpy()
libcublas.so
CUDA
Program
cublasSaxpy()
SASS code
PTX code
SASS code
(Virtual assembly)
Executable
./exe
</>
.nv_fatbin
.text
.nvFatBinSegment
SASS code
(Architecture
specific machine
code)
Notes: Let's walk through a simple example using cublasSaxpy().
This function is provided by the cuBLAS shared library. Inside that library are GPU kernels represented as SASS, NVIDIA's lowest-level machine code that executes directly on the GPU.
This SASS code is the attack target.
Importantly, we are not attacking model weights, application code, or framework code. We are targeting the SASS code of a shared library.
During compilation, CUDA code is translated to PTX and then to architecture-specific SASS. Then it is finally packaged into application's executable, inside the .nv_fatbin section you will find the SASS code.
Assume you have a CUDA program that uses cublasSaspy() function, this function belongs to cublas library, this is a shared lib which have the SASS code corresponding to the function. SASS code is the lowest level represention of machine code that run on GPU. This is what the attacker targets. Not model weights. Not application code. SASS instructions inside a shared library. The CUDA application is then further compiled down to PTX code which is then further compiled down to architecture specific machine code, and then wrapped into a executable. Inside this executable you will have nv_fatbin section that contain the SASS code which then run on the GPU

## Slide 11
CUDA accelerated libraries
CPU cores
CPU memory
GPU cores
GPU memory
1
3
2
./exe
</>
CUDA
Program
PTX code
SASS code
(Virtual assembly)
Executable
Notes: When the code is executed its first loaded into CPU memory. At runtime, when a function such as cublasSaxpy() is invoked, the corresponding SASS code is loaded and executed on the GPU.
If an attacker can corrupt these SASS instructions before execution, the GPU executes the corrupted code, causing incorrect computation and ultimately corrupting the application's output.
Next, we asked a simple question <Next slide>

## Slide 12
What happens if a Rowhammer bit-flip
lands inside a SASS instruction?
12

## Slide 13: Changes to SASS
Register change
MOV R1, c[0x0][0x20]
MOV R0, c[0x0][0x20]
0x4c98078000870001
0x4c98078000870000
Opcode change
FFMA R11, R22, R11, R8
FSET.F.FTZ.AND R11, R22, R11, !P0
0x5980040000b7160b
0x5880040000b7160b
Offset change
LDS.U.32 R23, [R17+0x140]
LDS.U.32 R23, [R17+0x148]
0xef4c100014071117
0xef4c100014871117
Instruction change
SHL R15, R3, 0x6
LOP3.LUT R15, R3, 0x6, R0, 0x48
0x384800000067030f
0x3c4800000067030
Observation: None of these cases trigger an exception or crash the kernel
Notes: Surprisingly, in most cases, a single-bit flip does not create an invalid instruction. Instead, it produces a different but still valid SASS instruction.
We observed four common outcomes.
First, a register change, where the instruction performs the same operation but uses a different register. The numbers represents the hexadecimal equivalent of the instruction encoding.
Second, an opcode change, where the operation itself changes—for example, a floating-point multiply-accumulate becomes a completely different instruction.
Third, an offset change, where a memory access is redirected to a nearby address.
And fourth, an instruction change, where the original instruction is transformed into another valid instruction.
The important observation is that none of these cases trigger an exception or crash the kernel.
The GPU continues execution normally and produces an output.
However, that output is now incorrect.
This is exactly what makes the attack effective the bit flip silently corrupts computation and degrades model accuracy.
The question is: how does the attacker actually identify vulnerable location to do bit flip? We'll answer that later in the talk when we discuss the practical challenges of the attack. Now lets connect all the dots.

## Slide 14
Connecting all the dots
Induce a bit-flip
in the SASS code of the CUDA library
while it resides in DRAM — before the victim executes.
How many ‘s’s are in “Strawberry”?
Asdf asdfasdrqwer Vadsfa SDfaqSDFADSF f,m.dsnalk;f
Asdklfj qawe[porouijlk; SADF MNALK/sd JFOI[PSDAJUF
Victim sees incoherent output text for the query
Notes: The attacker's goal is precise — flip one bit in the SASS code of the CUDA shared library while it is sitting in DRAM.
Timing matters: this must happen before the victim loads the library, so the corrupted version is what gets transferred to the GPU.
Once the attacker courrpts the SASS code, whenever the victim uses the model it will give incoherent response.

## Slide 15: PRowhammer: Requirements
Valid GPU instructions after bit-flip
GPU shared libraries accessible to attacker
ML Frameworks should use
GPU shared
libraries
ML Framework
Shared
Library
cuBLAS cuDNN
FFMA R11,R22, R11,R8
FSET.F.FTZ.AND R11, R22, R11,!P0 & 0x5
cuBLAS code page shared
Notes: To summarize, PRowhammer requires three conditions.
First, ML frameworks must rely on GPU shared libraries. This condition is easily satisfied—frameworks such as PyTorch and TensorFlow routinely invoke libraries like cuBLAS and cuBLASLt for core linear algebra operations.
Second, the attacker must be able to access the shared library pages that contain the GPU code and use them as Rowhammer targets.
Third, bit flips in SASS instructions must result in different but still valid instructions.
We've shown that all three conditions hold in practice.
As a result, PRowhammer is not just theoretically possible—it is a viable attack.
This brings us to the challenge:
How does the attacker identify the specific bit to flip in the library?

## Slide 16
Challenge
How does attacker identify which
bit to flip in shared library?
16
Notes: How does the attacker identify the specific bit to flip in the shared library?

## Slide 17
C2
GPU code in shared libraries is compressed
C1
Size of GPU shared libraries is in MBs, brute forcing bit-flip will take years
PRowhammer: Challenges
GPU shared library
0101001010101010101010101010101010110101010101110101010010101010101010010101010101010101010101010101010101010101010101010101011010101010111010101001010101010101001010101010101010101010101010101010101011010101010111010101001010101010101001010101010101010100
Compressed GPU code
Don't know where to flip?
Notes: Finding an exploitable bit flip is far from trivial because of two key challenges.
The first challenge is scale.
The .nv_fatbin section of cuBLASLt alone is about 255 MB, containing SASS code for many different GPU architectures.
Suppose we tried to test every bit. Even if a single test takes only 500 milliseconds—which is the time it takes inducing a bit flip and executing the kernel—the search would take roughly 11,800 days, or more than 32 years.
Clearly, brute force is not a practical strategy.
The second challenge is compression.
NVIDIA stores the .nv_fatbin section in a proprietary compressed format.
As a result, looking at the binary does not reveal where individual SASS instructions begin or end.
More importantly, a single bit flip in the compressed data often expands into multiple corrupted bits after decompression.
Instead of producing a clean modification to one instruction, it frequently generates invalid instructions and crashes the program.
So the challenge is not simply finding a bit flip—it is finding a bit flip that is both reachable and useful.

## Slide 18
0101001010101010101010101010101010110101010101110101010010101010101010010101010101010101010101010101010101010101010101010101011010101010111010101001010101010101001010101010101010101010101010101010101011010101010111010101001010101010101001010101010101010100
Run the target application
How to do bit-flip in compressed library?
Segment 1
Faulted Seg.
Segment 2
Segment N
Segment 4
Segment 5
Segment 6
1
2
Flip all the bits
SASS CODE
0101001010101010101010101010101010110101010101110101010010101010101010010101010101010101010101010101010101010101010101010101011010101010111010101001010101010101001010101010101010101010101010101010101011010101010111010101001010101010101001010101010101010100
GPU shared library
Target SASS code does not lie in the faulted segment
Application runs successfully with correct output
Application fails to run or produces incorrect output
Target SASS code lies in the faulted segment
C1
Notes: So how do we find an exploitable bit flip in a large compressed library?
Our key idea is to use a divide-and-conquer strategy.
We start with the entire GPU shared library containing the SASS code and partition it into segments.
Then, in an offline analysis step, we inject faults into all bits within one segment and execute the target application using the modified library.
We are not trying to reproduce these faults with Rowhammer at this stage. The goal is simply to identify which regions of the library influence the application's behavior.
If the application runs normally and produces the correct output, then the target SASS code is unlikely to be in that segment.
On the other hand, if the application crashes or produces incorrect output, then the target code must reside somewhere within the faulted segment.
We then interatively repeat the process on till we find a faulted segment
By doing this instead of searching billions of bits, we quickly zoom in on the small portion of the library that actually affects the target application.

## Slide 19
0101001010101010101010101010101010110101010101110101010010101010101010010101010101010101010101010101010101010101010101010101011010101010111010101001010101010101001010101010101010101010101010101010101011010101010111010101001010101010101001010101010101010100
Run the target application
How to do bit-flip in compressed library?
1
2
Randomly do single bit-flip
0101001010101010101010101010101010110101010101110101010010101010101010010101010101010101010101010101010101010101010101010101011010101010111010101001010101010101001010101010101010101010101010101010101011010101010111010101001010101010101001010101010101010100
Selected bit is not exploitable
Exploitable bit-flip location found!!
3
4
Application produces incorrect output
3
Faulted Seg.
Useful segment
0101001010101010101010101010101010110101010101110101010010101010101010010101010101010101010101010101010101010101010101010101011010101010111010101001010101010101001010101010101010101010101010101010101011010101010111010101001010101010101001010101010101010100
Application runs successfully with correct output
C2
Notes: Once we have identified a useful segment, the search becomes much more targeted.
We now perform random single-bit flips within that segment and execute the application.
If the application crashes or fails to run, we discard that bit and try another one.
If the application runs successfully, we compare its output against the expected output.
We try to find a bit flip that allows the application run to complete normally while producing an incorrect result.
That is exactly the behavior we are looking for.
Such a bit flip corresponds to an exploitable location: the program continues executing, but the underlying GPU computation has been silently corrupted.
Through this process, we can efficiently discover bit locations.

## Slide 20
End-to-End attack:
Attack on LLM
20
Notes: Now that we've seen how the attack works, let's look at the results.
We show an effect of PRowhammer on the LLaMA model and compare the model's response before and after the attack.
The only difference between these two executions is the targeted bit flip introduced by PRowhammer.

## Slide 21
Before PRowhammer
After
PRowhammer
Notes: As you can see, a single leads to model giving incoherent result.

## Slide 22
Transferability: Property of bit-flip location to affect multiple DNN models adversarially
Attack on LLM: Results
Model | GPU | Average F1_BERT (Pristine) | Average F1_BERT (Corrupt)
Llama-2-7B | RTX A6000 | 0.62 | 0.3
 | RTX 4090 | 0.62 | 0.26
 | RTX 5060 | 0.62 | 0.26
Mistral-7B | RTX A6000 | 0.58 | 0.3
 | RTX 4090 | 0.58 | 0.26
 | RTX 5060 | 0.58 | 0.26
Falcon-7B | RTX A6000 | 0.58 | 0.26
 | RTX 4090 | 0.58 | 0.3
 | RTX 5060 | 0.58 | 0.25
Notes: To evaluate PRowhammer, we tested three different LLMs: LLaMA, Mistral, and Falcon.
We also evaluated the attack across three different GPU platforms.
The table reports the BERTScore, which measures the semantic similarity between the model's output and the expected, or golden, output.
We use questions from the Google Natural Questions dataset as inputs to the models.
Before the attack, the outputs closely match the expected responses.
However, after inducing a single targeted bit flip, the average BERTScore drops to around 0.3.
A score this low indicates severe degradation and the generated text is often incoherent, irrelevant, or substantially different from the correct answer.

## Slide 23
End-to-End attack
Attack on Image Classification Model
23

## Slide 24
Image classification attack
After Attack :
DOG
Before Attack : CAT
Dog, Cat, Cow, Pig, Sheep, Horse, Goat, Deer, Chicken, Fish
Notes: We also evaluate PRowhammer on image classification models.
Here, the attacker's goal is straightforward: induce a bit flip that reduces the model's classification accuracy.

## Slide 25
Model | Dataset
ResNet-18 | CIFAR-10, MNIST, FMNIST and IMAGENET
ResNet-34 | 
ResNet-50 | 
VGG-16 | 
Image classification attack: Evaluation set
Notes: We evaluate the attack using the models and datasets shown on the slide.
The results are striking. In some cases, a single targeted bit flip is sufficient to reduce the model's classification accuracy all the way to 0%.

## Slide 26
Transferability: Property of bit-flip location to affect multiple DNN models adversarially
Transferability of exploitable bit-location
Do the exploitable bit-locations affect the models equally?
Question
Are there any universal bit-locations that affect all models in our setup?
Question
Notes: we also explored several interesting research questions.
For example, do exploitable bit-flip locations affect all models equally?
Are there universal bit locations whose corruption degrades multiple models across different workloads?
We investigate these questions in detail in the paper.

## Slide 27: Countermeasures
Code integrity verification after CPU-to-GPU transfer
Conventional Rowhammer defenses
  TRR [S&P ‘20]
  ECC memory
  Software isolation (CATT [USENIX Security ’17], SoftTRR [USENIX ATC ’22], Citadel [MICRO ‘25])
Notes: "Countermeasures fall into two categories. The first category is GPU-specific, the natural defense is to add integrity verification which should be performed after code transfer into GPU memory.
"The second category is conventional Rowhammer defenses — ECC memory, software isolation techniques like Citadel. These are all relevant and reduce risk. But none of them fully close the window. ECC on DDR5 has been shown to still be exploitable.
PRowhammer can only be fully mitigated if DRAM bit-flips are prevented altogether, or if CPU-to-GPU code transfers include integrity verification. Neither condition is met today.

## Slide 28: Summary
Observation:
  CPU DRAM lies in the critical path of GPU computation
  Shared libraries contain SASS code, in compressed form
Key idea and implementation:
  Inducing a bit-flip via Rowhammer in CUDA accelerated libraries containing SASS code, in order to corrupt GPU computation
Results
  Single bit-flip can make an LLM model give incoherent output, and degrade the image classification accuracy down to 0%
Notes: To Summarize We observe that CPU DRAM lies in the critical path of GPU computation shared libraries contain GPU SASS code in compressed form. Our key idea was to induce a bit-flip via Rowhammer in CUDA accelerated libraries in order to corrupt the GPU computation Single bit flip can make LLM model give incoherent output and degrade the image classification accuracy down to 0%

## Slide 29
Thank You
CASPER
Pioneering with grit, bit by bit
Artifact Available
Artifact Functional
Result Reproduced
भारतीय प्रौद्योगिकी संस्थान मुंबई
Indian Institute of Technology Bombay
ISCA 2026
Paper
Artifact
Notes: These are QR to our paper and artifact. Our artifact is open and I would encourage the audience to check it out Thank YOu

## Slide 30
Backup Slides
30

## Slide 31
Attacker
Induce a bit-flip
in the nv_fatbin section of a CUDA library
while it resides in DRAM — before the victim executes.
OS Page Deduplication
Frame Feng Shui
cuBLAS code page shared
Page Frame Cache
Linux buddy allocator
[Flip feng shui USENIX ’16]
[Rambleed S&P ’20]
Memory Massaging
Notes: The attacker's goal is precise — flip one bit in the nv_fatbin section of a CUDA shared library while it is sitting in DRAM.
Timing matters: this must happen before the victim loads the library, so the corrupted version is what gets transferred to the GPU.
The attacker has two paths to get the victim's physical library page within Rowhammer range.
If OS page deduplication is active, the OS automatically co-locates the attacker's and victim's copies of the library at the same physical address.
The attacker already has the page.
If deduplication is disabled, the attacker uses Frame Feng Shui — a technique from prior Rowhammer work that shapes the OS page allocator to steer the victim's page into a predictable physical location next to attacker-controlled rows. Either path leads to the same outcome: the attacker hammers, the bit flips, the SASS code is corrupted.

## Slide 32
Attacker Identifies
Flippable Page
Memory
Templating
1
Attacker
End-to-End Rowhammer Attack

## Slide 33
Attacker Identifies
Flippable Page
Memory Massaging
Page Frame Cache
Attacker Unmaps
Flippable Page
2
Memory
Templating
1
Attacker
End-to-End Rowhammer Attack

## Slide 34
Victim Process Requests a page
Attacker Identifies
Flippable Page
Memory Massaging
Page Frame Cache
Attacker Unmaps
Flippable Page
2
Hammering
4
Victim Maps
Flippable Page
3
Memory
Templating
1
Attacker
End-to-End Rowhammer Attack